## Slide 1: ELE1
REVISION NOTES

## Slide 2: Systems
Complex systems broken down into sub-systems.
Identify sub-systems in circuit diagrams.

## Slide 3: Logic Gates
NOT, AND, OR, NAND, NOR, EX-OR
Truth tables – every combination of inputs.

## Slide 4: Boolean Algebra

## Slide 5: Prefixes
giga ×1,000,000,000 (G) GHz
mega ×1,000,000 (M) MHz, M
kilo ×1,000 (k) kHz, k, kV
milli ×0.001 (m) mV, mA, mW
micro ×0.000 001 () V, A, W, F
nano ×0.000 000 001 (n) nF
pico ×0.000 000 000 001 (p) pF

## Slide 6: Voltage and Current
Voltage ACROSS object – Volts
Current THROUGH object – Amps
Power = Voltage x Current – Watts
Resistance = Voltage/Current - Ohms

## Slide 7: Series and Parallel
Series:-
  Current is the same
  Voltage is shared
Parallel:-
  Current is shared
  Voltage is the same

## Slide 8: Resistors
In series –
In parallel –
Colour Code
BS1852
Preferred values
Tolerance

## Slide 9: Diodes
Conventional current flow.
Allows current to pass in one direction.
0.7V across a forward biased silicon diode

## Slide 10: LEDs
Find the voltage across R.
Note the maximum current through the LED
Calculate R
Choose the next largest preferred value

## Slide 11: Zener Diodes
Note the maximum power of the zener
Calculate the maximum current
Calculate the voltage across R
Calculate R.
Choose the next largest preferred value

## Slide 12: Resistive Input Devices
LDR
  as light level increases, the resistance decreases
  Log-log graphs.
Thermistor
  As the temperature increases, the resistance decreases
  Log-lin graphs

## Slide 13: Voltage Dividers
This formula is not on the data sheet!

## Slide 14: Transistors and MOSFETs

## Slide 15: Output devices
Use protection diode with inductive devices
To remove large induced voltage
Diode protects semiconductor when the device is switched OFF
Motor
Relay
solenoid

## Slide 16: Operational Amplifier
Differential amplifier
Large input resistance 109
Large open-loop voltage gain, A,  106
Low output resistance  100
Frequency compensated
Gain-bandwidth product

## Slide 17: Comparator

## Slide 18: Capacitors
In series
In parallel

## Slide 19: RC networks.
Time Constant
  Time to charge to 0.63Vs
  Time to discharge to 0.37Vs
Time to charge to 0.5Vs=0.69RC
Time to fully charge or discharge = 5RC

## Slide 20: 555 Monostable
When the TRIGGER input goes below 1/3Vs
OUTPUT goes high and DISCHARGE switches off
C charges through R
Until capacitor voltage =2/3Vs (THRESHOLD voltage)
OUTPUT goes low and DISCHARGE switches on
Capacitor discharged.

## Slide 21: 555 astable
When first switched on, TRIGGER is less than 1/3Vs
OUTPUT goes high, DISCHARGE switches off
Capacitor charges through R1 and R2
Until capacitor voltage = 2/3Vs (THRESHOLD)
OUTPUT goes low, DISCHARGE switches on
Capacitor discharges through R2
Until capacitor voltage = 1/3Vs (TRIGGER)
OUTPUT goes high, process repeats